## Slide 1: Accelerated Stability Prediction for Biotherapeutic CASSS VEDG
Drago Kuzman
12-May 2026
RA CMC, TRD

## Slide 2: Disclaimer
These slides are intended for educational purposes only and for the personal use of the audience.
These slides are not intended for wider distribution outside the intended purpose without presenter approval.
The content of this slide deck is accurate to the best of the presenter’s knowledge at the time of production.

## Slide 3: Agenda
1 | Introduction to stability modeling
2 | Standard approach: extrapolation in time
3 | Alternative approach: extrapolation in temperature by Arrhenius (AKM)
4 | Model assumptions
5 | PoC for biological drugs

## Slide 4: Stability Studies of Biologics
Drug Candidate selection
Formulation screening
Shelf life-assessment of clinical material
Final formulation screening
Primary packaging screening
Formulation robustness
Out-of-fridge studies
Cumulative hold times studies
Shel-life claim of commercial drug
Post approval process changes
…

## Slide 5: Shelf-Life Determination of Commercial Biologics
ICH Q5C “ Primary data to support a requested storage period for either drug substance or drug product should be based on long-term, real-time, real-condition stability studies.”
Time (years)
QA (%)
end of shelf-life specifications
0
1
2
3
Shelf-life
Q5C Guideline.pdf

## Slide 6: ICH Q1 Stability Revision is in its Public Consultation Phase
Revision of ICH Stability training materials
- Consensus Building
- Develop draft guidance
- Draft guideline adopted
- Public Consultation
Step 1
Step 2
Step 3
Step 4
Step 5
- Adoption of final guideline (or revision)
- Implementation by Regulators
Sign-off by
Industry & Regulators
Endorsement
by ICH assembly
and Regulators
Sign-off by
Regulatory
Topic leads
Adopted by
Regulators
Concept Paper
Business Plan
Concept paper outline
developed by QDG
Dec 2020
Q2 2025 Q2 2027
May 2026
November 2026
From EFPIA
Annex II about enhanced stability modeling to claim a commercial shelf life beyond real data
June 2026

## Slide 7: Standard approach: Stability Extrapolation in Time Beyond Real Data
Long-term stability extrapolation of 6 months stability might not be reliable. Why?
At intendant storage condition 5°C, the degradation of biologics is notably slow, often requiring a year or more for a reliable determination.
The level of degraded biologics at 5°C stays within the variability range of analytical methods for several months.​
SEC Aggregates (%)
6 months data
3 years data
(%)
(%)

## Slide 8: Alternative approach (component 1): Extrapolation in Temperature by Arrhenius based modeling
Time
QA
40 °C
Extrapolation in Temperature | Time Factor for Ea=20 kcal/mol
40°C -> 25 °C | 5
40 ˘C -> 5 °C | 57
25°C -> 5 °C | 11
25 °C
t
5*t
Time
QA
40 °C
25 °C
t
5*t
57*t
5 °C
Time
QA
40 °C
t

## Slide 9: Alternative approach (component 2): Kinetic model of degradation profile
Time
QA
Zero order (linear) model
Time
QA
First order (exponential) model
N-order two step model
(Šesták–Berggren equation)
Time
QA
…

## Slide 10: Accelerated Predictive Stability for Biologics
Modellable stability indicating CQAs
Risk Assessment based on prior data and knowledge
Non-Modellable stability indicating CQAs
Reliable degradation model for most of QAs: Arrhenius based First-order (exponential) kinetic model
Key assumption: The model is trained using data generated under accelerated conditions, where the dominant degradation mechanism is the same as under the intended storage condition.

## Slide 11: Validation of Arrhenius Assumption Across All Conditions Used For Model Training
2021 Kuzman et al. Scientific Reports https://doi.org/10.1038/s41598-021-99875-9
Arrhenius plot
graphical representation of Arrhenius equation

## Slide 12: Different aggregation mechanism at higher temperature
Zidar et at., Scientific Reports 2025, https://doi.org/10.1038/s41598-025-07037-y
Ea1
Ea2

## Slide 13: Aggregation modeling (option 1): Two Steps Kinetics model
Wang & Roberts:, Non-Arrhenius Protein Aggregation, AAPS Journal, Vol. 15, No. 3, July 2013
T: 5°C - 65°C
Aggregation profiles can be modeled by using two steps Advanced Kinetic modeling:

## Slide 14: Aggregation modeling (option 2): First Order Kinetics Model
T [5 - 50 °C]
Ea = 59.6 kcal/mol
Accelerated stability data
Arrhenius plot
undersestimated

## Slide 15: Aggregation modeling (option 2): First Order Kinetics Model
T [5 - 50 °C]
Ea = 59.6 kcal/mol
T [5 - 45 °C]
Ea = 54.0 kcal/mol
Accelerated stability data
Arrhenius plot
undersestimated
undersestimated

## Slide 16: Aggregation modeling (option 2): First Order Kinetics Model
T [5 - 50 °C]
Ea = 59.6 kcal/mol
T [5 - 45 °C]
Ea = 54.0 kcal/mol
T [5 - 40 °C]
Ea = 21.4 kcal/mol
Accelerated stability data
Arrhenius plot
undersestimated
undersestimated

## Slide 17: Aggregation Can Be Reliably Modeled
Zidar et at., Scientific Reports 2025, https://doi.org/10.1038/s41598-025-07037-y
Long-term prediction at 5°C based on short term accelerated stability study
For robust Aggregation modeling it is key to know temperature threshold value allowing you to train the model by using a data from low temperature pathway.
Temperature threshold for mAb like formats is typically >40° C, for bi-valent nano body >35° C and for ScFv and DARpin >30° C.

## Slide 18: By proper temperature range selection one can reduce model complexity
Less model parameters (y0, yinf, A, Ea)
Increased model robustness
Reduced risk of overfitting
Less data required
Kuzman D., et al., Sci Rep. 2021 Oct 15;11(1):20534. doi: 10.1038/s41598-021-99875-9.
First Order Kinetic model

## Slide 19: PoC: Novartis examples with long term validation
2021 Kuzman et al. Scientific Reports https://doi.org/10.1038/s41598-021-99875-9
Bioassay
Aggregates
Acidic variants
nrCE-SDS purity
Percentage of validation data within 95% prediction interval
 | mAb1 | Rituximab | Etanercept | Adalimumab
CEX amount of main variants (%) | 100% | 91% | 100% | 99%
CEX sum of acid variants (%) | 100% | 97% | 100% | 99%
nrCE SDS purity (%) | 100% | 95% | 100% | 98%
nrCE SDS sum of fragments (%) | 100% | no data | no data | no data
Relative potency | n.a. | 97% | 100% | 100%
SEC purity (%) | 100% | 98% | 90% | 100%
SEC sum of aggregates (%) | 100% | 94% | 90% | 97%

## Slide 20: PoC: examples from >18 biologics product
Drug Product | State | Modality | Subtype | Concentration (mg/mL)
A | Liquid | mAb | IgG4 | Medium
B | Liquid | mAb | IgG1 | Medium
C | Liquid | mAb coform | IgG1 + IgG4 | Low
D | Liquid | mAb | IgG1 | High
E | Liquid | mAb | IgG4 | High
F | Liquid | ADC | IgG1 | Low
G | Lyophilized | ADC | IgG1 | Low
H | Liquid | mAb | IgG4 | Low
I | Lyophilized | mAb | IgG4 | Low
J | Liquid | mAb | IgG4 | High
K | Liquid | mAb | IgG1 | High
L | Liquid | mAb | IgG4 | Low
M | Liquid | mAb coform | IgG4 + IgG4 | Low
N | Liquid | mAb | IgG4 | Medium
O | Liquid | mAb | IgG1 | Medium
P | Liquid | mAb | IgG1 | Medium
Q | Liquid | mAb coform | IgG1 + IgG4 | Low
R | Lyophilized | Fusion Protein | N/A | Medium
Broad application of Arrhenius first order kinetic modeling across different biotherapeutic modalities.
2024 Dillon et al., Predicting the Long-Term Stability of Biologics with Short-Term Data, https://doi.org/10.1021/acs.molpharmaceut.4c00609
More examples: (Huelsmeyer, Kuzman et al. 2023),(Lennard, Zimmermann et al. 2024),(Dillon, Xu et al. 2024),(Kuzman, Bunc et al. 2021),(Bunc, Hadzi et al. 2022),(Doshi, Martin and Tomlinson 2020)

## Slide 21: Conclusions
Advance Kinetic Modeling of Stability for Biologics
Arrhenius equation enables extrapolation in temperature which leads to faster, precise long-term predictions from accelerated data
Different kinetic models can be applied, however “simpler is better”
For biological drug, most of the modellable quality attributes can be described by first order Arrhenius kinetics
Model Assumptions Validation
Goodness of fit
Extrapolation in temperature by Arrhenius plot and/or fir of independent data set from recommended storage condition to the predicted profile
Ongoing Verification
Fit of recommended storage condition data obtained after model finalized (e.g. post-approval)
Applications
Stability modeling supports candidate/formulation selection, temperature excursions, hold times, control strategy, shelf-life claims,…

## Slide 22: Thank you